## Slide 1
DIGGS · RIGID INCLUSION GROUND IMPROVEMENT
A Data Model for Rigid Inclusions
How project workflow — design, specification, construction, and post-installation verification — maps onto a connected, structured record.
Illustrated with a worked example: Riverside Embankment RI Foundation System

## Slide 2
THE PROBLEM
Today, a project's story is scattered across files that don't talk to each other
TODAY
– Design calculations — a spreadsheet or calc package
– Specifications & drawings — PDF and CAD
– Construction records — daily logs, as-built surveys
– Test reports — load tests, integrity tests — PDF
None of these reference each other in a way software can follow.
THE DIGGS WAY
– One structured record carries design intent, the limits it must satisfy, the reasoning behind it, and what was actually built and tested
– Every piece of data links back to what it came from
– “Did we build what we designed, and did it perform?” becomes a query — not an archaeology project
DIGGS is an existing, open exchange format for geotechnical data (borings, samples, lab & field tests). Rigid Inclusions extends it to ground improvement.
DIGGS Rigid Inclusion Data Model
2 / 18

## Slide 3
THE WORKFLOW
Every phase of the project has a home in the data model
DESIGN
What shall
be built
SPECIFICATION
What limits
must hold
CONSTRUCTION
What was
actually built
VERIFICATION
Did it
perform
BASIS
The engineering justification — governing standards, ground model, design method — underlies design and specification throughout.
This deck walks each of these four groups, then shows a small worked example that carries data through all of them.
DIGGS Rigid Inclusion Data Model
3 / 18

## Slide 4
THE PROGRAM
One RI Program holds three kinds of content
RigidInclusionProgram
DESIGN
Intent — what shall be built
– Column grid & spacing
– Diameter & length
– Platform thickness
SPECIFICATION
Constraint — what limits must hold
– Installation technique
– Tolerances
– Acceptance criteria
BASIS
Justification — what it's founded on
– Governing standards
– Design method
– Working life & safety format
A project can hold several programs — one per package, consultant, or contract phase — all built from the same three ingredients.
DIGGS Rigid Inclusion Data Model
4 / 18

## Slide 5
DESIGN SCOPE
A design can describe one feature — or an entire population
POPULATION SCOPE
zone + grid
A zone boundary plus a grid pattern (spacing, orientation) describes every column inside it — one design object, however many columns.
Site-wide layout: triangular grid @ 2.0 m · Ø450 mm · 12 m long → governs thousands of columns
INSTANCE SCOPE
1
one named feature
Some things are just named once — a specific platform, or the system as a whole.
LTP-North platform design — one named feature, one design
Same design object type either way — only the scope changes.
DIGGS Rigid Inclusion Data Model
5 / 18

## Slide 6
EXCEPTIONS
A local exception states only what's different
Zone design
Ø450 mm · 12 m long · triangular grid @ 2.0 m
Abutment exception
– 15 m long, reinforced to 6 m
diameter & grid inherited, not restated
based on →
Most specific wins. Change the parent design and every exception downstream still resolves correctly — nothing has to be re-entered.
DIGGS Rigid Inclusion Data Model
6 / 18

## Slide 7
WHAT GETS BUILT
Foundation system → platforms → columns
RI Foundation System
Load Transfer
Platform — North
Load Transfer
Platform — South
mandatory link
CMC-N-001
Rigid Inclusion
CMC-S-001
Rigid Inclusion
Which platform a column sits under is read from its position on the ground — not stored as a link. The platform's footprint decides membership.
Trial column
Proves the method before production relies on it. Built independent of any platform — no parent reference, by design.
DIGGS Rigid Inclusion Data Model
7 / 18

## Slide 8
ONE-WAY REFERENCES
The as-built cites its design — never the other way around
Design
issued first
As-built column
realized later
“was built to”
– A design file never has to be reissued each time a new column goes in the ground
– Records are never edited after delivery — only added to
– When a design is revised, older columns still correctly cite the version that governed them
Same rule, every relationship in DIGGS: every reference points backward, to what came before it.
DIGGS Rigid Inclusion Data Model
8 / 18

## Slide 9
THE BASIS
The engineering justification travels with the data
Governing standards
ASIRI, Eurocode 7
Design method
Arching model — Hewlett & Randolph
Working life
75 years
Safety format
EC7 — Design Approach 2
Consequence class
CC2
Every design and specification links to a Basis, so a reviewer years later sees not just what was designed, but why.
DIGGS Rigid Inclusion Data Model
9 / 18

## Slide 10
LIMITS & ACCEPTANCE
One flexible recipe covers every tolerance and performance limit
SUBJECT
STATISTIC
OPERATOR
LIMIT
BASIS
CONFORMANCE
plan position deviation
individual
≤
25 mm
per element
PERFORMANCE
settlement
mean
≤
threshold
per platform
Same shape whether it's checking a construction tolerance or a post-installation performance result — no one-off elements per limit type.
DIGGS Rigid Inclusion Data Model
10 / 18

## Slide 11
VERIFICATION
Test results are structured data, tied to a specific column
STATIC LOAD TEST
Applied load vs. head settlement, recorded as a data series.
0 → 1,400 kN · 0 → 16.2 mm
LOW-STRAIN INTEGRITY TEST
Relative impedance vs. depth — flags necking or voids along the column.
impedance 1.00 → 0.95 over 12 m
Each result cites the column it was measured on — so pass/fail traces back to one column, one design, one specification.
DIGGS Rigid Inclusion Data Model
11 / 18

## Slide 12
A WORKED EXAMPLE
Riverside Embankment — a small project, every concept present
Embankment settlement & stability improvement over soft ground
1
Foundation system
2
Load transfer platforms
3
Columns (2 production + 1 trial)
5
Design objects
1 + 1
Specification + acceptance criterion
1
Basis
2
Post-installation test results
DIGGS Rigid Inclusion Data Model
12 / 18

## Slide 13
EXAMPLE · DESIGN
Site-wide layout, plus a system-level performance target
RIColumnDesign
site-wide · population scope
– Triangular grid @ 2.0 m
– Ø450 mm · 12.0 m long
– 7% area replacement ratio
RISystemDesign
the embankment · instance scope
– Predicted settlement: 32 mm (total)
– Settlement efficacy: 0.62
RILTPDesign — North
– 0.60 m thick
– load efficacy 0.82
RILTPDesign — South
– 0.75 m thick
– load efficacy 0.79
All four design objects cite the same Basis and the same governing Specification.
DIGGS Rigid Inclusion Data Model
13 / 18

## Slide 14
EXAMPLE · AS-BUILT
One system, two platforms, three columns
Riverside Embankment RI Foundation System
LTP-North
0.60 m thick
LTP-South
0.75 m thick
CMC-N-001
12.0 m · Ø450 mm
CMC-S-001
12.0 m · Ø450 mm
Membership by geometry — position inside the platform's footprint — not a stored reference.
CMC-TRIAL-001
– 12.0 m · Ø450 mm
– No parent RIFS reference
built ahead of production to prove the method
DIGGS Rigid Inclusion Data Model
14 / 18

## Slide 15
EXAMPLE · TESTING
Prove the method, then confirm production quality
STATIC LOAD TEST
on CMC-TRIAL-001
– Loaded to 1,400 kN → 16.2 mm settlement
– Run before production relied on the method
the normal target for a trial column
LOW-STRAIN INTEGRITY TEST
on CMC-N-001
– Relative impedance 1.00 → 0.95 over 12 m depth
– A production column, checked after installation
no anomalies indicated
Both results are stored as data series and cite the exact column tested — traceable straight back to its design.
DIGGS Rigid Inclusion Data Model
15 / 18

## Slide 16
PUTTING IT TOGETHER
How it all connects
BASIS
DESIGN
intent
SPECIFICATION
constraint + acceptance criteria
PHYSICAL OBJECTS
RI Foundation System · Load Transfer Platform · Rigid Inclusion
POST-INSTALLATION TESTS
Test / Monitor results
Every arrow points back to what came before it, all the way up the chain — basis at the top, tests at the bottom.
DIGGS Rigid Inclusion Data Model
16 / 18

## Slide 17
WHY IT MATTERS
What this structure buys the project
Scales
Thousands of columns, a handful of design objects — not thousands of records.
Traceable
Every built column can answer “what was I designed to, and did I pass?” by following references, not searching PDFs.
Durable
Records are appended, never edited. Revision history is built in, not bolted on afterward.
Reusable
Rigid Inclusions is the pilot. The same design / specification / basis pattern extends to grouting, deep foundations, and other ground-improvement techniques.
DIGGS Rigid Inclusion Data Model
17 / 18

## Slide 18
Questions & Discussion
Schema validated against 130+ test cases, built as an extension of the existing DIGGS geotechnical data exchange standard.
DIGGS Rigid Inclusion Data Model
18 / 18