## Slide 1: Standardizing Rigid Inclusion Soil Improvement Data with DIGGS
Dr. Mohamed Ezzat

## Slide 2: Pre-Installation Phase

## Slide 3: Stage 1: Site Investigation Planning Pre-Installation
Plan a ground investigation program that is good enough to (a) confirm ground conditions, (b) quantify variability, and (c) support RI/CMC design (settlement and bearing) and constructability.
DIGGS - Feature
Report at end of stage (key parameters):
Investigation plan: number/location of boreholes and CPTs, target depths, sampling plan
Proposed lab test matrix (classification + strength + compressibility)
Groundwater measurement plan (standpipes/piezometers, monitoring period)
Utility clearance / access constraints
Health & safety plan for drilling and site access
Investigation schedule + responsible parties
<name attribute=“attribute value”>value</name>

## Slide 4: Stage 2: Field Site Investigation Execution Pre-Installation
Perform borings, CPT/CPTu (often very valuable for CMC), trial pits if needed, groundwater measurements, and obtain good quality samples.
DIGGS - Feature
Report at end of stage (key parameters):
Borehole logs: stratigraphy, sample depths, recovery, RQD (if rock), SPT N-values (if used)
CPT/CPTu logs: qc, fs, u2, inferred soil behavior type
Groundwater levels (date/time stamped) and installation details for piezometers
In-situ test results (vane shear, pressuremeter/dilatometer if done)
Any anomalies: fill pockets, obstructions, boulders, artesian conditions, contamination indicators
Coordinates and elevations of all investigation points
<name attribute=“attribute value”>value</name>

## Slide 5: Stage 3: Laboratory Testing and Soil Characterization Pre-Installation
Lab tests define engineering parameters: strength, compressibility, index properties, unit weights, permeability.
DIGGS - Feature
Report at end of stage (key parameters):
Index: moisture content, Atterberg limits, grain size distribution, unit weight
Strength: UU/CIU/CD triaxial, direct shear (as applicable), undrained shear strength Su correlations
Compressibility: oedometer/consolidation parameters (Cc, Cr, mv, Cv)
Chemical aggressivity (if durability/cement compatibility is relevant): sulfates, chlorides, pH
Summary statistics and variability by layer (mean, range, COV)
<name attribute=“attribute value”>value</name>

## Slide 6: Stage 5: Feasibility and Selection of CMC/RI as the Ground Improvement Solution Pre-Installation
Confirm that CMC/RI is the right solution versus alternatives (piles, stone columns, preloading, DSM, etc.).
DIGGS - Feature
Report at end of stage (key parameters):
Target performance criteria: allowable total settlement, differential settlement, bearing/stability targets
Concept options and screening rationale (cost/schedule/risk)
Constructability assessment (access, spoil, groundwater, obstructions)
Preliminary RI/CMC concept: approximate spacing, diameter, depth range, load transfer platform (LTP) concept
Key risks + mitigation (e.g., soft layers thickness uncertainty → additional investigation)
<name attribute=“attribute value”>value</name>

## Slide 7: Stage 6: Define Design Basis and Acceptance Criteria Pre-Installation
Set the “Acceptance Criteria” before detailed design and construction: what counts as compliant installation and compliant performance.
DIGGS - Feature
Report at end of stage (key parameters):
Structural loads and load combinations to be supported (service and ultimate)
Settlement criteria and monitoring locations
Minimum column toe level / required bearing layer definition
Minimum LTP thickness and material requirements (if known)
Installation acceptance metrics (examples):
  minimum depth / toe tolerance
  minimum grout volume ratio or expected theoretical vs actual take
  limits on withdrawal rate / pressure range
  verticality tolerance
Verification test types and preliminary frequencies (to be finalized with contractor)
<name attribute=“attribute value”>value</name>

## Slide 8: Stage 7: Detailed CMC/RI System Design (Owner/Engineer Design or Design-Assist) Pre-Installation
Design the CMC layout and LTP so the system meets settlement, bearing, and stability requirements.
DIGGS - Feature
Report at end of stage (key parameters):
Column geometry: diameter, target depth, toe criteria, head cut-off level
Layout: grid type (square/triangular), spacing, treatment footprint, edge detailing
Area replacement ratio (or equivalent) and design stress concentration assumptions
LTP design: thickness, gradation, compaction targets, reinforcement (geogrid) if required
Global stability checks (especially embankments)
Predicted performance: settlement estimate, differential settlement, factors of safety
Drawings + specs: coordinate-based plan, details, tolerances
<name attribute=“attribute value”>value</name>

## Slide 9: Stage 10: Trial Section / Test Columns (Optional) Installation
Install a small number of test columns to confirm constructability and to calibrate acceptance criteria.
DIGGS - Feature
Report at end of stage (key parameters):
Test column logs: depth, torque, rotation, penetration/withdrawal rate, grout pressure/volume
Observed issues: obstructions, grout losses, refusal, groundwater effects
Adjusted method parameters and updated acceptance criteria (if needed)
Initial verification results (e.g., early-age strength tests if applicable)
<name attribute=“attribute value”>value</name>

## Slide 10: Stage 8: Contractor Procurement and Method Statement Approval Pre-Installation
Select the specialty contractor and lock down the construction methodology and QA/QC plan.
DIGGS - Feature
Report at end of stage (key parameters):
Contractor qualifications and relevant RI/CMC experience
Equipment/method: displacement vs partial displacement; grout/concrete system; monitoring system
Proposed grout/mortar mix design and supply plan
Inspection & Test Plan (ITP): hold points, records, nonconformance process
Trial section plan and verification testing plan
Proposed production rate and sequencing plan
<name attribute=“attribute value”>value</name>

## Slide 11: B. Installation Phase

## Slide 12: Stage 9: Pre-Construction Site Preparation and Controls Installation
Prepare the site so the rig can work safely and consistently, and so columns go in the correct locations.
DIGGS - Feature
Report at end of stage (key parameters):
Working platform design and certification (bearing capacity, thickness, proof rolling)
Site grading, drainage, dewatering readiness (if needed)
Survey control: benchmarks, grid layout, coordinate system
Utilities clearance confirmation
Environmental controls (washout, spoil handling, grout spill plan)
Approved shop drawings and “Issued for Construction” package
<name attribute=“attribute value”>value</name>

## Slide 13: Stage 11: Production CMC Installation (Main Construction) Installation
Install the full production set of columns per design and method statement. This is where disciplined data capture is critical.
DIGGS - Feature
Report at end of stage (key parameters):
Per column (as-built record):
Unique column ID, coordinates (X/Y), ground level, cut-off level
Start/end time, rig ID/operator
Target depth vs achieved depth; toe stratum confirmation (how verified)
Installation method (tool type, displacement level)
Monitoring While Installing (typical):
  penetration rate and withdrawal rate
  torque (and/or crowd force)
  rotation speed
  grout/concrete pressure
  grout/concrete volume (and volume vs theoretical)
  pauses/stoppages and reasons
Deviations and nonconformances (e.g., short column, obstruction, abnormal grout take)
Corrective actions (re-drill, secondary column, local redesign)
<name attribute=“attribute value”>value</name>

## Slide 14: Stage 11: Production CMC Installation (Main Construction) Installation
Install the full production set of columns per design and method statement. This is where disciplined data capture is critical.
DIGGS - Feature
Report at end of stage (key parameters):
Production summary statistics (weekly/end-of-stage):
Total columns installed vs planned
% meeting each acceptance criterion
List of exceptions + resolutions
Material consumption totals and trends
<name attribute=“attribute value”>value</name>

## Slide 15: Stage 12: Column Head Treatment (Caps) and Platform Interface Works Installation
Caps or Trim/cut columns to level, protect heads if needed, and prepare for LTP placement.
DIGGS - Feature
Report at end of stage (key parameters):
Final head elevation distribution (as-built)
Head condition and any repairs
Confirmation of spacing tolerance / positional tolerance (survey)
Any damaged columns and remediation steps
Integrity tests (if any)
<name attribute=“attribute value”>value</name>

## Slide 16: Stage 13: Load Transfer Platform (LTP) Construction Installation
Place and compact the granular LTP; install geogrid if designed.
DIGGS - Feature
Report at end of stage (key parameters):
LTP thickness (design vs as-built) and level survey results
Material certification:
  Gradation
  fines content
  moisture content range
  source and quality tickets
  Compaction results:
    target relative compaction (%MDD) or density index
    in-place density tests (locations and results)
Geogrid/geotextile details (if used): type, strength, overlap, placement photos
Proof rolling/plate load test results if specified
<name attribute=“attribute value”>value</name>

## Slide 17: C. Post-Installation

## Slide 18: Stage 14: Verification Testing Program Post-Installation
Prove the system meets requirements. Typically combines “column quality” verification and “system performance” verification.
DIGGS - Feature
Report at end of stage (key parameters):
Test matrix executed vs planned (type, number, locations)
Column verification results (depending on spec/contractor method), such as:
  coring results (diameter/continuity, material quality)
  compressive strength test results (if samples/cubes are used)
  integrity observations (method-dependent)
Load testing (if specified):
    column load tests or zone load tests
    plate load tests on LTP (if required)
    load–settlement curves, interpreted stiffness, acceptance statement
Nonconformances + corrective works + retest outcomes
<name attribute=“attribute value”>value</name>

## Slide 19: Stage 15: Performance Monitoring and Final Acceptance Post-Installation
Confirm the system performs as expected under construction loads and/or early service loads (especially for embankments).
DIGGS - Feature
Report at end of stage (key parameters):
Settlement monitoring results (time vs settlement) at agreed points
Differential settlement checks (adjacent points)
Pore pressure readings (if piezometers used) and trends
Any trigger/action levels exceeded and actions taken
Final acceptance statement linked to criteria in Stage 6
<name attribute=“attribute value”>value</name>

## Slide 20: Stage 16: Closeout and Handover Post-Installation
Deliver a clean as-built package so the owner can reuse the data and so future teams can learn from the project.
DIGGS - Feature
Report at end of stage (key parameters):
Complete as-built dataset: every column + LTP + test results + monitoring records
Summary of compliance: pass/fail counts, exceptions and resolution
Final drawings (as-built layout), certifications, and signed QC/QA package
Lessons learned and recommended improvements for future projects
<name attribute=“attribute value”>value</name>

## Slide 21: Summary of the Parameters for DIGGS

## Slide 22
[REQ] = minimum fields that should exist for a usable RI/CMC dataset
[REC] = strongly recommended for QA/QC, analytics, and interoperability
[OPT] = optional (project‑specific or nice to have)

## Slide 23: Pre-Installation
A. Project and dataset metadata
[REQ] ProjectID (unique string; persistent) [REQ] ProjectName [REQ] Owner / Client [REQ] SiteName / LocationName [REQ] CoordinateReferenceSystem (EPSG code or WKT) [REQ] VerticalDatum [REQ] UnitsPolicy (explicit; SI/US customary; preferably SI internally) [REQ] DatasetVersion / RevisionID [REQ] AuthoringOrganization [REQ] DataCreationDateTime (ISO 8601) [REC] SpecificationVersion / ContractPackageID [REC] DesignEngineer / GeotechnicalEngineerOfRecord [REC] ContractorName (if known at this stage)

## Slide 24: Pre-Installation
B. Ground model linkage (site investigation and design parameters)
(We don’t need to repeat full logs if they already exist in DIGGS SI data, but you must link the RI design to them.)
[REQ] ReferenceToInvestigationData (IDs/links to boreholes/CPTs/lab tests used)
[REQ] DesignGroundwaterLevel (elevation; plus basis: seasonal high/mean)
[REQ] GoverningSoilLayers (IDs or names; thickness ranges)
[REC] DesignParameterProfiles (per layer or depth-dependent):
  Su(z) or strength parameters (Su, φ’, c’)
  Compressibility (mv, Cc/Cr, Cv)
  Stiffness (E or equivalent)
[OPT] GeohazardFlags (soft pockets, organic, liquefaction susceptibility, obstructions risk)

## Slide 25: Pre-Installation
C. RI/CMC design intent (what was designed)
C1. Treatment area / zones (recommended as a “TreatmentArea” feature)
[REQ] TreatmentAreaID
[REQ] TreatmentAreaBoundaryGeometry (polygon)
[REQ] GroundImprovementPurpose (enumeration; settlement control / bearing / stability / etc.)
[REC] ZoneType (building slab / embankment / tank / platform)
[REC] TargetPerformanceCriteria
  MaxTotalSettlement (mm)
  MaxDifferentialSettlement / AngularDistortion (mm or ratio)
  FactorOfSafetyTargets (bearing/stability)

## Slide 26: Pre-Installation
C2. CMC layout and geometry (design values)
[REQ] DesignInclusionType (RigidInclusion / CMC)
[REQ] PatternType (square / triangular / custom)
[REQ] DesignSpacingS (m)
[REQ] DesignDiameterD (m)
[REQ] DesignDepth / ToeElevation (m or elevation)
[REQ] CutoffElevation (planned column head level)
[REQ] EndBearingLayerDefinition (text + layer ID)
[REC] EdgeTreatmentDetails (half‑spacing, perimeter rows, transitions)
[REC] AreaReplacementRatio (dimensionless)
[REC] DesignStressConcentrationAssumption (dimensionless, if used)
[OPT] DesignMethodReference (unit‑cell / numerical / project method memo)

## Slide 27: Pre-Installation
C3. Load Transfer Platform (LTP) design intent
[REQ] LTP_ID
[REQ] LTP_ThicknessDesign (m)
[REQ] LTP_MaterialType (granular fill / engineered fill)
[REQ] LTP_GradationLimits (spec band or reference)
[REQ] LTP_CompactionRequirement (e.g., %MDD or relative density)
[REC] LTP_ReinforcementFlag (yes/no)
[REC] GeosyntheticType (geogrid/geotextile)
[REC] GeosyntheticStrengthProperties (as specified)
[OPT] LTP_StiffnessTarget (Ev2 / modulus target)

## Slide 28: Pre-Installation
D. Construction plan and acceptance criteria (the “rules”)
[REQ] InstallationMethodPlanned (full displacement / partial displacement / predrill + tremie / etc.)
[REQ] Grout/ConcreteMixDesignID (reference)
[REQ] TargetProductionTolerances
  PositionTolerance (mm)
  VerticalityTolerance (% or mm/m)
  DepthTolerance (m)
[REQ] AcceptanceCriteriaSetID (reference)
[REC] TrialSectionRequired (yes/no; and limits)
[REC] PlannedVerificationTests
  type + frequency + locations logic
[OPT] EnvironmentalConstraints (spoils handling, washout plan, etc.)

## Slide 29: Installation
This is the core of RI/CMC value. In DIGGS terms, treat each CMC as a Feature with geometry, plus an InstallationActivity with time series or summarized metrics.
A. Rig / equipment / monitoring system metadata
[REQ] RigID [REQ] MonitoringSystemName/Version (if digital logging used) [REQ] OperatorID (or crew ID) [REC] ToolType (auger type, diameter, bit) [REC] CalibrationRecords (flow meter, pressure sensor calibration date) [OPT] WeatherConditions (if relevant for grout)
B. Material batching and delivery (linked to columns)
[REQ] MaterialBatchID [REQ] MaterialType (grout / mortar / concrete) [REQ] BatchDateTime [REQ] BinderType (cement type) [REQ] WaterCementRatio (or mix proportions) [REC] Admixtures (type + dosage) [REC] FreshProperties (slump/flow, density, temperature) [OPT] SupplierTicketID

## Slide 30: Installation
This is the core of RI/CMC value. In DIGGS terms, treat each CMC as a Feature with geometry, plus an InstallationActivity with time series or summarized metrics.
C. Per‑column “header” (minimum as‑built identity + geometry)
[REQ] InclusionID (unique, persistent) [REQ] TreatmentAreaID (link) [REQ] PlannedX, PlannedY [REQ] AsBuiltX, AsBuiltY (survey or rig GNSS) [REQ] GroundSurfaceElevationAtInstall [REQ] StartDateTime / EndDateTime [REQ] PlannedDepth vs AchievedDepth [REQ] CutoffElevationAchieved [REQ] InstallationMethodActual (enumeration) [REQ] Status (installed / replaced / rejected / reworked)

## Slide 31: Installation
D. Per‑column installation records (summaries)
These can be recorded either as time series (preferred) or as summary values (minimum).
Minimum summary metrics
[REQ] TotalInjectedVolume (m³) [REQ] VolumePerMeter (m³/m) (or equivalent) [REQ] MaxInjectionPressure (kPa or bar) [REQ] AverageInjectionPressure [REQ] WithdrawalRateAverage (m/min) [REC] PenetrationRateAverage (m/min) [REC] MaxTorque / AverageTorque (kN·m) [REC] RotationSpeedAverage (rpm) [REC] MaterialBatchIDUsed (link)

## Slide 32: Installation
Termination / refusal information
[REQ] TerminationType (design depth reached / refusal / obstruction / other)
[REQ] TerminationDepth / Elevation
[REC] TerminationReasonDetail (free text + code list)
[REC] ObstructionEncounteredFlag (yes/no; depth)
Nonconformance + corrective action
[REQ] NonconformanceFlag (yes/no)
[REQ] NonconformanceType (short column / low take / high take / deviation / etc.)
[REQ] CorrectiveAction (re-drill / additional column / redesign / accept as-is)
[REC] EngineerDispositionID (approval/refusal record)

## Slide 33: Installation
E. Installation time‑series (strongly recommended)
If the rig logs continuously, store time series keyed by timestamp and depth.
[REC] Depth(t) or Depth vs Time
[REC] PenetrationRate(t)
[REC] WithdrawalRate(t)
[REC] Torque(t)
[REC] RotationSpeed(t)
[REC] CrowdForce/Downforce(t) (if available)
[REC] PumpPressure(t)
[REC] FlowRate(t)
[REC] CumulativeVolume(t)
[OPT] GroutTemperature(t)
[OPT] Vibration/Noise metrics (if recorded)

## Slide 34: Post-Installation
A. As‑built RI/CMC inventory summary
[REQ] TotalInstalledCount
[REQ] InstalledByZoneCount
[REQ] ExceptionsList (IDs)
[REC] StatisticalSummaries (depth/volume/pressure distributions)
[REC] AsBuiltSpacingCheckResults (min/mean/max spacing; outliers)
B. Column head treatment and survey
[REQ] FinalHeadElevation (per column or per cluster)
[REQ] PositionSurveyResult (per column)
[REC] HeadCondition (good / damaged / repaired)
[OPT] HeadProtectionDetails (cap, lean concrete, etc.)

## Slide 35: Post-Installation
C. LTP construction (as‑built + QC)
[REQ] LTP_AsBuiltThicknessMap (spot checks with coordinates)
[REQ] MaterialSourceID
[REQ] GradationTestResults (IDs; location/date)
[REQ] CompactionTestResults (density/moisture; location/date)
[REC] GeosyntheticAsBuilt (type, roll IDs, overlaps, photos reference)
[OPT] PlateLoad / ModulusTestResults (Ev2 or equivalent)

## Slide 36: Post-Installation
D. Verification testing (columns and/or system)
You may not do all of these on every project, but the schema should support them.
Column verification
[REQ] VerificationTestID [REQ] TestType (coring / UCS / integrity / excavation exposure / etc.) [REQ] AssociatedInclusionID(s) [REQ] TestDateTime [REQ] ResultSummary + PassFail [REC] CoreDetails (if coring): core length, recovery %, observed defects measured diameter UCS results (MPa) + specimen metadata [OPT] IntegrityMethodDetails (if used; method‑specific fields)

## Slide 37: Post-Installation
D. Verification testing (columns and/or system)
Load testing (if required)
[REQ] LoadTestID
[REQ] TestType (single inclusion / group / zone / plate)
[REQ] LoadSteps (kN) + hold times
[REQ] SettlementMeasurements (mm vs time/load)
[REQ] AcceptanceCriteriaReference
[REC] InterpretedStiffness/Capacity (project-defined)

## Slide 38: Post-Installation
E. Performance monitoring time‑series (if instrumentation exists)
[REQ] InstrumentID (settlement plate, extensometer, piezometer, inclinometer)
[REQ] InstrumentType
[REQ] Location (X,Y,Z)
[REQ] ReadingDateTime
[REQ] ReadingValue + Units
[REC] TriggerLevels (alert/action thresholds)
[REC] EventsLog (construction stage, embankment lift height, loading milestones)
[OPT] AutomatedDataFeedMetadata (if IoT)

## Slide 39: Post-Installation
F. Remediation / rework records
[REQ] RemediationActionID
[REQ] Trigger (why remediation was required)
[REQ] ActionType (additional column / replacement / local redesign / etc.)
[REQ] LinkedInclusionIDs
[REQ] VerificationAfterRemediation (test ID + pass/fail)

## Slide 40: Post-Installation
G. Final acceptance package fields
[REQ] AcceptanceDate
[REQ] AcceptanceAuthority (name/role)
[REQ] ComplianceStatement (met all criteria / exceptions accepted)
[REQ] FinalAsBuiltDatasetReference (file set ID / repository tag)

## Slide 42: Thank You
Mohamed Ezzat